PREPARED BY

B.HEMAKUMAR

SUCCESSIVE APPROXIMATION A/D CONVERTER

FEATURES:

- Most popular.

- More complex circuitry than COUNTER type, but much shorter conversion time.

- Conversion time is a constant i.e. independent of the value of the analog input.

CONSTRUTION DETAILS:

- It doesn’t use a counter to provide input to D/A converter.

- It uses a 8 bit register called Successive Approximation Register (SAR) Motorola MC 14549

- D/A converter: MC 1408

BLOCK DIAGRAM OF SUCCESSIVE APPROXIMATION A/D CONVERTER:

Block diagram consists of

  - D/A converter

  - Programmer

  - Converter

  - Clock

  - Comparator

Function: Its output is used for setting and resetting the bits at the output of programmer.

WORKING:

- Programmer sets MSB to 1 with all bits to 0.

- Comparator compares the D/A output with analog input.

- If D/A output is large, then comparator output goes low.

- MSB reset to 0.

- If D/A output is small, then comparator output is high.

- MSB is kept 1 itself and second MSB is set to 1.

- Thus 1 is tried in each bit of D/A decoder until at end of this process, binary equivalent of analog signal is obtained.

- Process requires 1 clock period/bit.

- Conversion time: N clock signals or step for N bits.

ILLUSTRATION FOR A 4 BIT SAR A/D CONVERTER:

  - Initially control logic circuit resets all flip-flops Q0 to Q7.

  - MSB is set to 1, thereby signal reaching the ladder is 1000

  - Voltage produced by ladder is now compared with analog inputs.

  - If Vref  < Analog

      - Then comparator output gives signal to control logic to reduce the Vref accordingly, i.e. Q6 = 1. Digital signal now becomes 1100.

  - Once again equivalent analog voltage is compared with input signal.

  - If Vref  > Analog

      - Then comparator output gives signal to control logic as

Q7 = 0 & Q6 = 1. The digital signal will now be 0100.

  - Process repeats until Analog input = Vref.

REFERENCE:

“ Digital fundamentals” by Basavaraj.