## Specifications

| Market Position: DeskBook Leading Performance: Intel Desktop CPU Processor , Intel Chipset 845PE support FSB-533, DDR-333 SO-DIMM, 4x AGP, discrete VGA design with upgradeable VGA daughter board Intel Chipset 845GV(FSB533, DDR-266) with UMA VGA support DT 15” XGA or NB 15” SXGA+ or 16” UXGA/SXGA+ LCD Form Factor: 3-spindle design, brand new ID Wireless: 802.11b or 802.11a/b Mini PCI Solution, Storage: DT 3.5” 5400/7200 rpm HDD or NB 2.5” 9.5 mm HDD Combo (DVD+CD-RW) 24x10x8x24, 8x DVD or 24x CD-ROM. Cost-Effective: 6-layer mother board design with desktop components User-Friendly: Handler design No Battery Processor & Core logic CPU: Intel Desktop P4/Celeron 1.7Ghz ~ 3.06GHz FCPGA TDP 82W support, Hyper-Thread ready North Bridge: Dual layout reserved for Intel 845 PE and Intel 845GV South Bridge: ICH4 with USB 2.0 support Weight and Dimension: 353.6 x 300.5 x 51.9mm (15” DT LCD, 3.5” HDD), 4.0 kg 353.6 x 300.5x 48.4mm (16” NB LCD, 3.5”HDD),4.2 kg Display DT 15”XGA and NB 15” SXGA & 16” UXGA/SXGA+ LCD nVidia GeForce4 420/440 Go VGA Chip and embedded 32/64 MB DDR graphic memory on daughter card Simultaneous LCD and CRT display at non-interlace external CRT Dual View support 3D video and 4x AGP support Support TV-Out System Memory Two DDR SoDIMM socket up to 1024 MB 512KB FLASH BIOS with boot block; shadow RAM support Storage Subsystem 40/80/60/120/200 GB DT 3.5” HDD up to 7200rpm ; 20G/40GB NB 9.5 mm 2.5” HDD Module bay for Combo (24x10x8x24), DVD (8x) or CD-ROM(24x), 12.7 mm Internal 1.44-MB, 3.5-inch FDD CardBus One Type-III Power Subsystem ACPI Compliant 150W AC adapter | Keyboard and Pointing Device 84/85/88-key, inverted "T" cursor layout Built-in touchpad pointing device; located at the center of the palm rest with large two buttons below the Touchpad. 12 function keys; 4 cursor keys; separate PgUp, PgDn, Home, End keys; two Windows keys; hotkey controls Embedded numeric keypad International language support Scroll key for internet Audio System AC-97 audio system with two speakers SPDIF support for option SoundBlaster-Pro and MS-Sound System compatible Super Audio DJ control with small LCD panel for option V.92 Communications 56Kbps ITU standard fax/modem in MDC module Ethernet Connection: IEEE 802.3 10/100 BaseT Ethernet LAN built-in Wireless LAN: 802.11a or 802.11a/b build in mini-PCI Solution I/O Ports One PCMCIA type-III sockets One RJ45 jack for Ethernet One RJ11 56Kbps fax/modem One DC-IN jack for AC adapter One TV-out port One external VGA port One speaker/headphone-out jack support SPDIF Line in One Mic in Four USB 2.0 port One IEEE 1394 port One PS/2 One Serial Port One Parallel Port Two card reader port, MS and SD Software/Firmware Support Window XP Home and Windows XP Professional compliant, |
| --- | --- |