FORCED RCL

By Reinaldo Baretti Machin

www.geocities.com/serienumerica

The differential equation is

L di/dt + R i  + q/C  =  V0 cos( ω t)          (1)

Transforming it into a difference equation , gives

q2=2.*q1-q0 + dt**2*( -q1/(L*c) -(R/L)*curr+vgen(t-dt)/L)       (2)

The intial conditions are    q 0   and   i 0 = (dq/dt)0

or   q 0  and   q1 =  q 0 +   (∆ t) i 0     .

c RLC circuit

real L

data R , L ,C , Vcero/ 50. ,12.0E-3, 1.e-5, 6./

c      qexact(t)=qcero*exp(-R*t/(2.*L))*cos(omegap*t)

vgen(t)=vcero*cos(wg*t)

vc(q)=q/C

VL(q0,q1,q2)= L *(q2-2.*q1+q0)/dt**2

VR(q2,q1)= R *(q2-q1)/dt

pi=2.*asin(1.)

q0=0.

c      qcero=q0

c     initial current is zero

q1=q0

wg=1./sqrt(L*c)

c      omegap=sqrt( 1./(L*c) - (r/(2.*L))**2)

t1=L/R

t2=sqrt(L*c)

tscale =amin1(t1,t2)

tfinal=2.*2.*pi/wg

dt=tscale/100.

nstep=int(tfinal/dt)

kp=int(float(nstep)/70.)

kount=kp

Print*,'R,L,C=',R, L, C

print*,'dt,t1,t2,nstep=',dt,t1,t2,nstep

print*,'t      ,      vc,     vL ,    vr,    vgen'

print*,'    '

print 100 ,0.,vc(q0),Vgen(0.),vr(q1,q0),vgen(0.)

c      print 100 ,0. , q0

do 10 i=2,nstep

t=dt*float(i)

curr=(q1-q0)/dt

q2=2.*q1-q0 + dt**2*( -q1/(L*c) -(R/L)*curr+vgen(t-dt)/L)

if(i.eq.kount)then

print 100, t,vc(q2),VL(q0,q1,q2),vr(q1,q0),vgen(t)

kount=kount+kp

endif

q0=q1

q1=q2

10    continue

100   format(1x,'t,vc,vr =', 5(3x,e10.3))

stop

end

# Text boxes

-8

w(gen) = 10. w (resonance)

inductive circuit

Vgenerator

VR

VL

VC

volts

t(s)

5.00E-02

3.00E-02

1.00E-02

02

-1.00E-

10

5

0

-5

-10

w(gen) = (0.1) w (resonance)

capacitive circuit

-6

-4

-2

0

2

4

6

8

-1.00E-04

1.00E-04

3.00E-04

5.00E-04

t(s)

volts

VC

VL

VR

Vgenerator