Motion of Meteoritic Dust Particles

by Reinaldo Baretti Machín

www.geocities.com/serienumerica2

www.geocities.com/serienumerica

reibaretti2004@yahoo.com

Reference:

1. Classical Mechanics: Dover Publications,2nd Edition by H.C. Corben and Philip Stehle , page 73.

### 2. Poynting-Robertson effect , From Wikipedia , http://en.wikipedia.org/wiki/Poynting-Robertson_effect

### The equation of motion for meteoritic dust particles suject  to radiation pressure from the sun and to relativistic mass accretion is

### (1)

### The second term in parenthesis is the force of the radiation assuming total absorption  , the last term proportional to the velocity v ,is the force due to relativistic accretion of mass. In general the ,first two terms , the radial force, are dominant.

### As long as  GMm > (dE/dt) A /(4πc) the orbits are elliptical. But for a set of fixed initial conditions the period is longer than for the same problem without radiation pressure.

### The radiation pressure is the main term when

### m < (dE/dt) A /(4πcGM)                                                                . (2)

### It destroys the elliptical orbits blowing away the particles.

### To find the particle size we let  m ~ ρ a3  where ρ is the density of iron 7.8E3 kg/m3 and a is the size of the particle. Also A ~ a2  and dE/dt =3.78E26 watts ,

### G=6.67E-11Nm2/kg2   , c=3E8m/s  ; then

### a <  dE/dt /(4πcGM ρ) = 1.E-7 m  ie. 10 micrometers          . (3)

To test the effect of particle size  on the orbit  we integrate numerically the equation of motion for particles of sizes equal to  1 micro meter , .5E-6 m, .3E-6 m and .5E-7 m.

All particle trajectories have the same initial conditions

namely   (x0,y0)= (1.5E11 m,  0.)

v0=1.5e4 m/s , with the velocity initial angle 90 deg. with respecto to the X axis.

Only the last particle (size=.5E-7 m) is blown away. The others have increasingly larger periods as the mass diminishes.

c the Poynting Robertson effect meteoritic dust particles in the

c  gravitaional field of the sun  Reference Classical Mechanics,Corben

c    and Stehle , Dover Publications page 73

c needs an equation for dm/dt ,ie.the mass of the particle is variable?

real m , msun

data size,msun , G /.1e-6 ,1.98e30 ,6.67e-11  /

data c, edot ,drock/3.e8,3.78e26 , 7.8e3/

c alfa(initial velocity angle) is in degrees

data x0,y0,v0 , alfa/1.50e11,0.,1.5e4,90. /

ax(x,y,vx)=-(G*Msun -(Edot*area)/(4.*pi*c*m))*

$ (x/(x**2+y**2)**(3./2.)) -

$((edot*area)/(4.*pi*(x**2+y**2)*c**2*m))*vx

ay(x,y,vy)= -(G*Msun -(Edot*area)/(4.*pi*c*m))*

$ (y/(x**2+y**2)**(3./2.)) -

$((edot*area)/(4.*pi*(x**2+y**2)*c**2*m))*vy

pi=2.*asin(1.)

area=size**2

alfa=alfa*pi/180.

m=drock*size**3

tpress=m*v0*4.*pi*c*(x0**2+y0**2)/(edot*area)

taccret=m*4.*pi*c**2*(x0**2+y0**2)/(edot*area)

tkepler=sqrt((x0**2+y0**2)**(1.5)/(G*msun))

tscale=amin1(tpress, taccret,tkepler)

print*,'tpress, taccret,tkepler=',tpress, taccret,tkepler

print*,'size(m)=',size

print*,'  '

dt=tscale/150.

tfinal=50.*tscale

nstep=int(tfinal/dt)

kp=int(float(nstep)/80.)

kount=kp

vx=v0*cos(alfa)

vy=v0*sin(alfa)

x1=vx*dt+x0

y1=vy*dt+y0

print 100 ,0.,x0,y0

do 10  i=2,nstep

t=dt*float(i)

m=m+dt*(edot*area)/(4.*pi*(x1**2+y1**2)*c**2)

x2=2.*x1-x0+dt**2*ax(x1,y1,vx)

y2=2.*y1-y0+dt**2*ay(x1,y1,vy)

if(i.eq.kount)then

print 100 ,t,x0,y0

c      print*,((Edot*area)/(4.*pi*c*m))*

c     $ (y2/(x2**2+y2**2)**(3./2.)) ,((edot*area)/(4.*pi*

c     $(x2**2+y2**2)*c**2*m))*vx

kount=kount+kp

endif

x0=x1

x1=x2

y0=y1

y1=y2

vx=(x2-x1)/dt

vy=(y2-y1)/dt

10      continue

100   format(1x,'t,x,y=',3(4x,e10.3))

stop

end