3 Network Transmission Media

| 1 | List the Guided and and Unguaided media use in transmission of data Guided Media: twisted pair conductor, coaxial cable and fiber glass cable Unguided Media: Electro magnetic waves : e.g. radio waves (many bands), microwave, cellular telephone network, blue-tooth |
| --- | --- |
| 2 | Describe a) twisted pair b) coaxial c) fiber glass transmission medium . a) Twisted pair consist of pairs of twisted copper wires. The pairs can be shielded (STP) but the the unshielded twisted pair (UTP are more popular. (#6) b) Coaxial cable consist of a cylindrical copper core conductor which transmits electrical waves. The copper core is insulated and shielded. (#7) c) Fiber glass cable: consists of a fine glass or plastic cable which is used to conduct pulses of electromagnetic waves. (#9) |
| 3 | Compare the characteristics of UTP, coaxial and fiber optics Cable Cost : UTP (cheapest), coaxial (medium cost) and fiber optics (highest) Installation cost: UTP cheapest, coaxial moderate and fiber optics highest Electro Magnetic Interferences : UTP highest, coaxial low, fiber optics none. Bandwidth : UTP is low, Coaxial is high, fiber optics is highest.(#13)_ |
| 4 | What are wireless media. Wireless media is sometimes used instead of cables. Explain why? Radio waves, cellular phones and terrestrial microwave, satellite microware and infrared. (#17) Not feasible to lay cable because of environment or too costly to lay cables. Wireless is used. |
| 5 | Microwaves transmits in straight lines. How are the waves transmit over long distances? a) Use satellite to cover a wide geographical area (some remote areas). (#18) b) A chain of land based transmission towers. Transmit to antenna on buildings (#19) |
| 6 | Describe a cellular telephone or mobile phone network? (#22) Consists of a number of cells (or localities). Each cell has a transmission station which connects to the phone within its localities. |

| 7 | For what devices are infra-red device used? a) Remote control (TV) b) Computer and Personal Digital Assistance Transmit in straight line. Must point device and have no obstacle. |
| --- | --- |
| 8 | Describe a wireless application protocol network (WAP)? Use 2 way radio waves for local devices to access the internet (internet server) #24. Device may be computer, laptop and Personal Digital Assistant and router |
| 9 | Describe a broadband wireless system? # Deliver internet services over a wide area (homes and businesses) Transmit voice, video and data using high frequency radio waves. Bypass the local telephone line. |
| 10 | Describe a bluetooth system? (#27) Wireless system using a radio frequency 2.4GH. Short range like home, offices. Can be used to transfer signals between devices which are blue-tooth enabled. e.g. telephone, computer, printer, modem, mouse, personal data assistance. Up to 10m Can penetrate wall (unlike infra-red). |
| 11 | What factors are considered in selecting a media? a) cost b) speed c) distance and extending distance d) environment e)security b) Distance can be extended by using a repeater or amplifier e) Is the transmission media affected by noise (interference)? Can the transmission media be tapped? |