## Slide 1: Chapter 1: Computer Systems
Presentation slides for
Java Software Solutions
Foundations of Program Design
Second Edition
by John Lewis and William Loftus
Java Software Solutions is published by Addison-Wesley
Presentation slides are copyright 2000 by John Lewis and William Loftus. All rights reserved.
Instructors using the textbook may use and modify these slides for pedagogical purposes.

## Slide 2: Focus of the Course
Object-Oriented Software Development
  problem solving
  program design and implementation
  object-oriented concepts
    objects
    classes
    interfaces
    inheritance
    polymorphism
  graphics and Graphical User Interfaces
  the Java programming language

## Slide 3: Computer Systems
We first need to explore the fundamentals of computer processing
Chapter 1 focuses on:
  components of a computer
  how those components interact
  how computers store and manipulate information
  computer networks
  the Internet and the World-Wide Web
  programming and programming languages
  graphic systems

## Slide 4: Hardware and Software
Hardware
  the physical, tangible parts of a computer
  keyboard, monitor, wires, chips, data
Software
  programs and data
  a program is a series of instructions
A computer requires both hardware and software
Each is essentially useless without the other

## Slide 5: CPU and Main Memory
Central
Processing
Unit
Main
Memory
Chip that executes program commands
Intel Pentium III
Sun Sparc Processor
Primary storage area for programs and data that are in active use
Synonymous with RAM

## Slide 6: Secondary Memory Devices
Floppy Disk
Hard Disk
Main
Memory
Central
Processing
Unit
Secondary memory
devices provide
long-term storage
Information is moved
between main memory
and secondary memory
as needed
Hard disks
Floppy disks
ZIP disks
Writable CDs
Tapes

## Slide 7: Input / Output Devices
Monitor
Keyboard
Main
Memory
Central
Processing
Unit
Floppy Disk
Hard Disk
I/O devices allow user
interaction
Monitor screen
Keyboard
Mouse
Bar code scanner
Light pen
Touch screen

## Slide 8: Software Categories
Operating System
  controls all machine activities
  provides the user interface to the computer
  manages resources such as the CPU and memory
  Windows 98, Windows NT, Unix, Linux, Mac OS
Application program
  generic term for any other kind of software
  word processors, missile control systems, games
Most operating systems and application programs have a graphical user interface (GUI)

## Slide 9: Analog vs. Digital
There are two basic ways to store and manage data:
Analog
  continuous, in direct proportion to the data represented
  music on a record album - a needle rides on ridges in the grooves that are directly proportional to the voltage sent to the speaker
Digital
  the information is broken down into pieces, and each piece is represented separately
  music on a compact disc - the disc stores numbers representing specific voltage levels sampled at various points

## Slide 10: Digital Information
Computers store all information digitally:
  numbers
  text
  graphics and images
  audio
  video
  program instructions
In some way, all information is digitized - broken down into pieces and represented as numbers

## Slide 11: Representing Text Digitally
For example, every character is stored as a number, including spaces, digits, and punctuation
Corresponding upper and lower case letters are separate characters
H i , H e a t h e r .
72 105 44 32 72 101 97 116 104 101 114 46

## Slide 12: Binary Numbers
Once information is digitized, it is represented and stored in memory using the binary number system
A single binary digit (0 or 1) is called a bit
Devices that store and move information are cheaper and more reliable if they only have to represent two states
A single bit can represent two possible states, like a light bulb that is either on (1) or off (0)
Combinations of bits are used to store values

## Slide 13: Bit Combinations
1 bit
0
1
2 bits
00
01
10
11
3 bits
000
001
010
011
100
101
110
111
4 bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Each additional bit doubles the number of possible combinations

## Slide 14: Bit Combinations
Each combination can represent a particular item
There are 2N combinations of N bits
Therefore, N bits are needed to represent 2N unique items
21 = 2 items
22 = 4 items
23 = 8 items
24 = 16 items
25 = 32 items
1 bit ?
2 bits ?
3 bits ?
4 bits ?
5 bits ?
How many
items can be
represented by

## Slide 15: A Computer Specification
Consider the following specification for a personal computer:
  600 MHz Pentium III Processor
  256 MB RAM
  16 GB Hard Disk
  24x speed CD ROM Drive
  17” Multimedia Video Display with 1280 x 1024 resolution
  56 KB Modem
What does it all mean?

## Slide 16: Memory
Main memory is divided into many memory locations (or cells)
9278
9279
9280
9281
9282
9283
9284
9285
9286
Each memory cell has a numeric address, which uniquely identifies it

## Slide 17: Storing Information
9278
9279
9280
9281
9282
9283
9284
9285
9286
Large values are
stored in consecutive
memory locations
10011010
Each memory cell stores a set number of bits (usually 8 bits, or one byte)

## Slide 18: Storage Capacity
Every memory device has a storage capacity, indicating the number of bytes it can hold
Capacities are expressed in various units:
KB 210 = 1024
MB 220 (over 1 million)
GB 230 (over 1 billion)
TB 240 (over 1 trillion)
Unit Symbol Number of Bytes
kilobyte
megabyte
gigabyte
terabyte

## Slide 19: Memory
Main memory is volatile - stored information is lost if the electric power is removed
Secondary memory devices are nonvolatile
Main memory and disks are direct access devices - information can be reached directly
The terms direct access and random access are often used interchangeably
A magnetic tape is a sequential access device since its data is arranged in a linear order - you must get by the intervening data in order to access other information

## Slide 20: RAM vs. ROM
RAM - Random Access Memory (direct access)
ROM - Read-Only Memory
The terms RAM and main memory are basically interchangeable
ROM could be a set of memory chips, or a separate device, such as a CD ROM
Both RAM and ROM are random (direct) access devices!
RAM should probably be called Read-Write Memory

## Slide 21: The Central Processing Unit
A CPU is also called a microprocessor
It continuously follows the fetch-decode-execute cycle:
fetch
Retrieve an instruction from main memory
decode
Determine what the
instruction is
execute
Carry out the
instruction

## Slide 22: The Central Processing Unit (CPU)
The CPU contains:
Arithmetic / Logic Unit
Registers
Control Unit
Small storage areas
Performs calculations and decisions
Coordinates processing steps

## Slide 23: The Central Processing Unit
The speed of a CPU is controlled by the system clock
The system clock generates an electronic pulse at regular intervals
The pulses coordinate the activities of the CPU
The speed is measured in megahertz (MHz)

## Slide 24: Monitor
The size of a monitor (17") is measured diagonally, like a television screen
Most monitors these days have multimedia capabilities: text, graphics, video, etc.
A monitor has a certain maximum resolution , indicating the number of picture elements, called pixels, that it can display (such as 1280 by 1024)
High resolution (more pixels) produces sharper pictures

## Slide 25: Modem
Data transfer devices allow information to be sent and received between computers
Many computers include a modem, which allows information to be moved across a telephone line
A data transfer device has a maximum data transfer rate
A modem, for instance, may have a data transfer rate of 56,000 bits per second (bps)

## Slide 26: Networks
A network is two or more computers that are connected so that data and resources can be shared
Most computers are connected to some kind of network
Each computer has its own network address, which uniquely identifies it among the others
A file server is a network computer dedicated to storing programs and data that are shared among network users

## Slide 27: Network Connections
Each computer in a network could be directly connected to each other computer in the network
These are called point-to-point connections
This technique is not feasible for
more than a few close machines
Adding a computer requires
a new communication line
for each computer already
in the network

## Slide 28: Network Connections
Most modern networks share a single communication line
Adding a new computer to the network is relatively easy
Network traffic must take
turns using the line, which
introduces delays
Often information is broken
down in parts, called packets,
which are sent to the receiving
machine then reassembled

## Slide 29: Local-Area Networks
LAN
A Local-Area Network
(LAN) covers a small
distance and a small
number of computers
A LAN often connects the machines
in a single room or building

## Slide 30: Wide-Area Networks
LAN
A Wide-Area Network (WAN)
connects two or more LANs,
often over long distances
A LAN is usually owned
by one organization, but
a WAN often connects
different groups in
different countries
LAN

## Slide 31: The Internet
The Internet is a WAN which spans the entire planet
The word Internet comes from the term internetworking, which implies communication among networks
It started as a United States government project, sponsored by the Advanced Research Projects Agency (ARPA), and was originally called the ARPANET
The Internet grew quickly throughout the 1980s and 90s
Less than 600 computers were connected to the Internet in 1983; now there are over 10 million

## Slide 32: TCP/IP
A protocol is a set of rules that determine how things communicate with each other
The software which manages Internet communication follows a suite of protocols called TCP/IP
The Internet Protocol (IP) determines the format of the information as it is transferred
The Transmission Control Protocol (TCP) dictates how messages are reassembled and handles lost information

## Slide 33: IP and Internet Addresses
Each computer on the Internet has a unique IP address, such as:
204.192.116.2
Most computers also have a unique Internet name, which is also referred to as an Internet address:
  renoir.villanova.edu
  kant.breakaway.com
The first part indicates a particular computer (renoir)
The rest is the domain name, indicating the organization (villanova.edu)

## Slide 34: Domain Names
The last section (the suffix) of each domain name usually indicates the type of organization:
edu
com
org
net
- educational institution
- commercial business
- non-profit organization
- network-based organization
Sometimes the suffix
indicates the country:
New suffix categories
are being considered
uk
au
ca
se
- United Kingdom
- Australia
- Canada
- Sweden

## Slide 35: Domain Names
A domain name can have several parts
Unique domain names mean that multiple sites can have individual computers with the same local name
When used, an Internet address is translated to an IP address by software called the Domain Name System (DNS)
There is no one-to-one correspondence between the sections of an IP address and the sections of an Internet address

## Slide 36: The World-Wide Web
The World-Wide Web allows many different types of information to be accessed using a common interface
A browser is a program which accesses and presents information
  text, graphics, sound, audio, video, executable programs
A Web document usually contains links to other Web documents, creating a hypermedia environment
The term Web comes from the fact that information is not organized in a linear fashion

## Slide 37: The World-Wide Web
Web documents are often defined using the HyperText Markup Language (HTML)
Information on the Web is found using a Uniform Resource Locator (URL):
http://www.lycos.com
http://www.villanova.edu/webinfo/domains.html
ftp://java.sun.com/applets/animation.zip
A URL indicates a protocol (http), a domain, and possibly specific documents

## Slide 38: Problem Solving
The purpose of writing a program is to solve a problem
The general steps in problem solving are:
  Understand the problem
  Dissect the problem into manageable pieces
  Design a solution
  Consider alternatives to the solution and refine it
  Implement the solution
  Test the solution and fix any problems that exist

## Slide 39: Problem Solving
Many software projects fail because the developer didn't really understand the problem to be solved
We must avoid assumptions and clarify ambiguities
As problems and their solutions become larger, we must organize our development into manageable pieces
This technique is fundamental to software development
We will dissect our solutions into pieces called classes and objects, taking an object-oriented approach

## Slide 40: The Java Programming Language
A programming language specifies the words and symbols that we can use to write a program
A programming language employs a set of rules that dictate how the words and symbols can be put together to form valid program statements
Java was created by Sun Microsystems, Inc.
It was introduced in 1995 and has become quite popular
It is an object-oriented language

## Slide 41: Java Program Structure
In the Java programming language:
  A program is made up of one or more classes
  A class contains one or more methods
  A method contains program statements
These terms will be explored in detail throughout the course
A Java application always contains a method called main
See Lincoln.java (page 26)

## Slide 42: Java Program Structure
public class MyProgram
{
}
// comments about the class
class header
class body
Comments can be added almost anywhere

## Slide 43: Java Program Structure
public class MyProgram
{
}
public static void main (String[] args)
{
}
// comments about the class
// comments about the method
method header
method body

## Slide 44: Comments
Comments in a program are also called inline documentation
They should be included to explain the purpose of the program and describe processing steps
They do not affect how a program works
Java comments can take two forms:
// this comment runs to the end of the line
/* this comment runs to the terminating
symbol, even across line breaks */

## Slide 45: Identifiers
Identifiers are the words a programmer uses in a program
An identifier can be made up of letters, digits, the underscore character (_), and the dollar sign
They cannot begin with a digit
Java is case sensitive, therefore Total and total are different identifiers

## Slide 46: Identifiers
Sometimes we choose identifiers ourselves when writing a program (such as Lincoln)
Sometimes we are using another programmer's code, so we use the identifiers that they chose (such as println)
Often we use special identifiers called reserved words that already have a predefined meaning in the language
A reserved word cannot be used in any other way

## Slide 47: Reserved Words
The Java reserved words:
abstract
boolean
break
byte
byvalue
case
cast
catch
char
class
const
continue
default
do
double
else
extends
false
final
finally
float
for
future
generic
goto
if
implements
import
inner
instanceof
int
interface
long
native
new
null
operator
outer
package
private
protected
public
rest
return
short
static
super
switch
synchronized
this
throw
throws
transient
true
try
var
void
volatile
while

## Slide 48: White Space
Spaces, blank lines, and tabs are collectively called white space
White space is used to separate words and symbols in a program
Extra white space is ignored
A valid Java program can be formatted many different ways
Programs should be formatted to enhance readability, using consistent indentation
See Lincoln2.java and Lincoln3.java

## Slide 49: Programming Language Levels
There are four programming language levels:
  machine language
  assembly language
  high-level language
  fourth-generation language
Each type of CPU has its own specific machine language
The other levels were created to make it easier for a human being to write programs

## Slide 50: Programming Languages
A program must be translated into machine language before it can be executed on a particular type of CPU
This can be accomplished in several ways
A compiler is a software tool which translates source code into a specific target language
Often, that target language is the machine language for a particular CPU type
The Java approach is somewhat different

## Slide 51: Java Translation and Execution
The Java compiler translates Java source code into a special representation called bytecode
Java bytecode is not the machine language for any traditional CPU
Another software tool, called an interpreter, translates bytecode into machine language and executes it
Therefore the Java compiler is not tied to any particular machine
Java is considered to be architecture-neutral

## Slide 52: Java Translation and Execution
Java source
code
Machine
code
Java
bytecode
Java
interpreter
Bytecode
compiler
Java
compiler

## Slide 53: Development Environments
There are many development environments which develop Java software:
  Sun Java Software Development Kit (SDK)
  Borland JBuilder
  MetroWork CodeWarrior
  Microsoft Visual J++
  Symantec Café
Though the details of these environments differ, the basic compilation and execution process is essentially the same

## Slide 54: Syntax and Semantics
The syntax rules of a language define how we can put symbols, reserved words, and identifiers together to make a valid program
The semantics of a program statement define what that statement means (its purpose or role in a program)
A program that is syntactically correct is not necessarily logically (semantically) correct
A program will always do what we tell it to do, not what we meant to tell it to do

## Slide 55: Errors
A program can have three types of errors
The compiler will find problems with syntax and other basic issues (compile-time errors)
  If compile-time errors exist, an executable version of the program is not created
A problem can occur during program execution, such as trying to divide by zero, which causes a program to terminate abnormally (run-time errors)
A program may run, but produce incorrect results (logical errors)

## Slide 56: Introduction to Graphics
The last one or two sections of each chapter of the textbook focus on graphical issues
Most computer programs have graphical components
A picture or drawing must be digitized for storage on a computer
A picture is broken down into pixels, and each pixel is stored separately

## Slide 57: Representing Color
A black and white picture can be stored using one bit per pixel (0 = white and 1 = black)
A color picture requires more information, and there are several techniques for representing a particular color
For example, every color can be represented as a mixture of the three primary colors Red, Green, and Blue
In Java, each color is represented by three numbers between 0 and 255 that are collectively called an RGB value

## Slide 58: Coordinate Systems
Each pixel can be identified using a two-dimensional coordinate system
When referring to a pixel in a Java program, we use a coordinate system with the origin in the upper left corner
Y
X
(0, 0)
(112, 40)
112
40