## Slide 1
Resistance
Part 1
Reference Book: Circuit Analysis by Robbins & Miller

## Slide 2
1 Resistance of Conductors (p. 60)
The resistance of a material is dependent upon several factors:
Type of materials
Length of the conductor
Cross-sectional area
Temperature

## Slide 3
The factors governing the resistance of a conductor at a given temperature:
where  = resistivity, in ohms-meters ( -m ) [Table 1]
l = length, in meters (m)
A = cross-sectional area, in square meters (m2)

## Slide 4
Table 1 Resistivity of Materials (p. 60)
MATERIAL RESISTIVITY, ,
AT 20oC (-m)
______________________________
Silver 1.645 x 10-8
Copper 1.723 x 10 -8
Gold 2.443 x 10 -8
Aluminum 2.825 x 10 -8
Tungsten 5.485 x 10 -8
Iron 12.30 x 10 -8
Lead 22 x 10 -8
Mercury 95.8 x 10 -8
Nichrome 99.72 x 10 -8

## Slide 5
MATERIAL RESISTIVITY, ,
AT 20oC (-m)
_____________________________
Carbon 3500 x 10 -8
Germanium 20 - 2300*
Silicon 500*
Wood 108 - 1014
Glass 1010 - 1014
Mica 1011 - 1015
Hard rubber 1013 - 1016
Amber 5 x 1014
Sulphur 1 x 1015
Teflon 1 x 1016

## Slide 6
Example 1 (p. 61)
EXAMPLE 1 Most houses use solid copper wire having a diameter of 1.63mm to provide electrical distribution to outlets and light sockets. Determine the resistance of 75 meters of a solid copper wire having the above diameter.
Solution We will first calculate the cross-sectional area of the wire
using equation 2.
A = πd2/4
= π(1.63 x 10-3 m)2/4
= 2.09 x 10-6 m2
Now, using Table 1, the resistance of the length of wire is found as
R = ρl/A
= (1.723 x 10-8 Ωm)(75m)/2.09 x 10-6m2
= 0.619 Ω

## Slide 7
Example 2 (p. 61)

## Slide 8
Question:
Two copper wires with same volume has radius r1 and r2 respectively. Find the ratio of their resistance.
Solution :
[ In Forms of R1, R2 (ohms) ]
Same vol => A1L1 = A2L2 or

## Slide 9
2. Temperature Effects (p. 69)
Resistance of a conductor is not constant at all temperature.
As temperature increasers, more electrons will escape their orbits, causing additional collisions within the conductors. For most conducting materials, the increase in the number of collisions translates into an increase in resistance.
The rate at which the resistance of a material changes with a variation in temperature is called the temperature coefficient of the material (  ). [Fig. 3.6]

## Slide 10
Fig. 3-6 Temp effects on the resistance of a conductor (p. 69)
2
1

## Slide 11
Resistance of any material increases as temp increases - positive temp coefficient.
For semiconductor materials, increases in temp allow electrons to escape their usually stable orbits and become free to move within the material. Hence resistance decreases as temp rises - negative temp coefficient. [Table 3.4, p. 70]
TABLE 3-4 Temperature Intercepts and Coefficients for Common Materials
T  (oC)-1  (oC)-1
(oC) AT 20oC AT 0oC
Silver -243 0.003 8 0.004 12
Copper -234.5 0.003 93 0.004 27
Aluminum -236 0.003 91 0.004 24
Tungsten -202 0.004 50 0.004 95
Iron -162 0.005 5 0.006 18

## Slide 12
TABLE 3-4 Temperature Intercepts and Coefficients for Common Materials
T  (oC)-1  (oC)-1
Lead -224 0.004 26 0.004 66
Nichrome -2270 0.000 44 0.000 44
Brass -480 0.002 00 0.002 08
Platinum -310 0.003 03 0.003 23
Carbon -0.000 5
Germanium -0.048
Silicon -0.075

## Slide 13
From Fig. 3-6, slope of the line
m = R/  T
= (R1 - 0) / (T1 - T) [unit :  / oC]
Define temp. coefficient as
1 = m / R1 [unit: (oC)-1]
Question: What is the sign (+ve or -ve) of the slope, m, for
a) copper?
b) silicon?

## Slide 14
The temp coefficient will not be constant everywhere but is dependent upon the resistance R1 and temp.
R2 = R1 + m T
= R1 + m (T2 - T1)
= R1 [ 1 + (m/R1)(T2 - T1)]
R2 = R1 [ 1 + (1)(T2 - T1)]
Therefore, knowing the resistance and temp coefficient at temp T1 can calculate the unknown resistance at temp T2.

## Slide 15
EXAMPLE 3-8 (p. 71)
An aluminum wire has a resistance of 20  at room temperature (20 C). Calculate the resistance of the same wire at temperatures of –40 C, 100 C, and 200 C.
Solution
At –40 C:
From Table 3-4, we see that aluminum has a temperature coefficient of  = 0.00391. The resistance at –40 C is now determined to be
R –40 C = (20  ){1 + [0.00391(C) –1] [–40 C –20 C]}
= 15.3 
[Learning Check IV]