## Slide 1
Electrical Quantities

## Slide 2
Electricity appears in one of two forms which are called negative and positive electricity. Electrical charge is the excess of negative or positive electricity on a body or in space. If the excess is negative, the body is said to have a negative charge and vice versa.
All matter consists of large numbers of particles termed molecules, being the smallest pieces of matter that can exist separately. Molecules can be subdivided into atoms and comprise one or more atoms bonded together.
An atom is the smallest particle of matter that can take part in a chemical change.
Electrical Charge

## Slide 3
All atoms consist of three basic constituent parts:
1. Electrons;
2. Protons; and
3. Neutrons.
An electron is an elementary particle charged with a small and constant quantity of negative electricity.
A proton is similarly defined but charged with positive electricity whilst the neutron is uncharged and is therefore neutral.
In an atom, the number of electrons normally equals the number of protons; it is the number of protons that determins to which element type the atom belongs.

## Slide 4
An atom can have one or more electrons added to it or taken away. This does not change its elemental classification but it disturbs its electrical balance. If the atom has excess electrons, it is said to be negatively charged. A charged atom is called an ion.
A body containing a number of ionised atoms is also said to be electrically charged.
It can be shown that positively- and negatively-charged bodies are mutually attracted to one another while similarly charged bodies repel one another.

## Slide 5: Electric Current - Movement of Electron
All electrons have a certain potential energy. Given a suitable medium in which to exist, they move freely from one energy level to another and his movement, when undertaken in a concerted manner, is termed an electric current flow.
Conventionally it is said that the current flows from a point of high energy level to a point of low energy level. These points are said to have high potential and low potential respectively.
For convenience the point of high potential is termed the positive and the point of low potential is termed negative, hence conventionally a current is said to flow from positive to negative potential.

## Slide 6
The transfer of electrons takes place more readily in a medium in which atoms can readily release electrons, e.g. copper, aluminium and silver. Such material is termed a conductor.
A material that does not readily permit electron flow is termed an insulator. e.g. porcelain, nylon and rubber.
There is also a family of materials termed semiconductors which have certain characteristices that belong to neither of the other groups.

## Slide 7: Electromotive Force (EMF) and Potential Difference (PD)
The emf represents the driving influence that causes a current to flow The emf is not a force but represents the energy expended during the passing of a unit charge through the source; an emf is always connected with energy conversion.
The energy introduced intro a circuit is transferred to the load unit by the transmission system, and the energy transferred due to the passage of unit charge between two points in a circuit is termed the potential difference (pd). If all the energy is transferred to the load unit, the pd across the load unit is equal to the source emf.
Both emf and pd are similar quantities. However, an emf is always active in that it tends to produce an electric current in a circuit whilst a pd may be either passive or active. A pd is passive whenever it has no tendency to create a current in a circuit.

## Slide 8
Electric Charge
It is defined that the quantity of electricity transferred in one second by a current of one ampere.
Symbol: Q
Unit: coulomb (C)
Q = I t
Definition, Symbol and Abbreviation

## Slide 9
Electric Current
It is defined that when electrons flowing through each of two parallel conductors spaced from one metre apart in vacuo and of infinite length, give rise to a force between the conductors of 2 x 10-7 newtons per metre run.
Symbol: I
Unit: ampere (A)
Definition, Symbol and Abbreviation

## Slide 10: It is defined the difference of potential between two points of a conducting wire carrying a constant current of one ampere, when the power dissipated between these two points is one watt. Symbol: V Unit: volt (V)
Electric Potential (PD)

## Slide 11
EMF has the symbol E but has the same unit of PD.
Symbol: E
Unit: volt (V)
Electromotive Force (EMF )