## Slide 1: Capacitance
1. Capacitor
The basic structure of a capacitor consists of
two parallel metal plates
separated by an insulating material
connection wires
Metal Plate
Wire
Insulation
Fig. 1

## Slide 2: Capacitance
The insulation is also called the dielectric.
Common examples of dielectric used in a capacitor are
Air
Ceramic
Mica
In a circuit diagram a capacitor is represented by the symbol
Fig. 2

## Slide 3: Capacitance
A direct current (dc) voltage source is connected to a capacitor with the polarity as shown.
Electron flows from the negative terminal towards the lower plate.
The lower plate becomes negatively charged
Fig. 3

## Slide 4: Capacitance
Electrons are drawn from the upper plate towards the positive terminal.
The upper plate becomes positively charges.
For an ideal dielectric no electron can flow through it.
An electric field is established between the two plates.
Fig. 4

## Slide 5: Capacitance
The amount of electric charge in the upper and lower plates are equal.
When the switch is open, the electrons are trapped in the metal plates.
They cannot flow through the dielectric or the external circuit.
Fig. 5

## Slide 6: Capacitance
The resistance of a practical dielectric is very high but not infinite causing a leakage current.
The electrons in the lower plate gradually moves to the upper plate through the dielectric.
Eventually the capacitor becomes completely discharged.
The discharge of the capacitor can be activated by connecting the capacitor to an external circuit as shown.
Fig. 6
+

## Slide 7: Capacitance
2. Capacitance
The charge Q accumulated in a capacitor is related to the applied voltage by
where C is the capacitance in unit of farad (F) and V is the voltage in volt.

## Slide 8: Capacitance
The capacitance C is dependent on the area of the metal plates and the property of the dielectric.
where A is the area of the metal plate and d is the distance separating the plates;  is the permittivity of the dielectric in unit of F/m

## Slide 9: Capacitance
The permittivity  of a dielectric may also be expressed as
where r is the relative dielectric constant and o is the free space permittivity with a value of 8.854x10-12 F/m.
Examples of relative dielectric constant r:
air 1
mica 5
polystyrene 2.5

## Slide 10: Capacitance
Work must be done to increase the charge in a capacitor.
The energy transferred to the capacitor is stored in the electric field between the metal plates.
The amount of work done to increase the charge by q is Vq.
The total work done to charge a capacitor C to Q coulomb
is joules .
This is the energy stored in a capacitor with a capacitance C charged to V volts.

## Slide 11: Capacitance
3. Capacitor Characteristics
The characteristics of a capacitor is specified by
(i) capacitance
(ii) capacitance tolerance
(iii) voltage rating
(iv) temperature coefficient

## Slide 12: Capacitance
(i) Capacitance
The capacitance of a capacitor may range from a few pF (10-12F) to thousands of F (10-6F) .
The capacitors available in the market are in discrete capacitance values similar to resistor values.
Capacitors with precise capacitance are costly.
A specific capacitance value can be formed by connecting capacitors in parallel and series.

## Slide 13: Capacitance
(ii) Capacitance Tolerance
Due to variation in material property and dimension the actual value of a capacitor may deviate from the nominal value.
Manufacturers specify the nominal value of a capacitor and its tolerance which is expressed in percentage e.g.
33 F  10%
In this example the actual value of the capacitor is in the range from 29.7 F to 36.3 F.

## Slide 14: Capacitance
(iii) Breakdown Voltage
The voltage across a capacitor creates an electric field across the dielectric.
The force acting on the electrons of the atoms of the dielectric is proportional to the applied field.
When the field strength is strong enough, the electrons may be torn away from the atoms causing a current to flow through the dielectric.
This is referred to as dielectric breakdown and causes permanent damage to the capacitor.

## Slide 15: Capacitance
The voltage at which the dielectric breakdown takes place is called the breakdown voltage.
The breakdown voltage depends on the property and the thickness of the dielectric.
The breakdown voltage ranges from a few volts to thousands of volts.
In the selection of capacitors for a given circuit the breakdown voltage must exceed the maximum voltage that may exist in the circuit.

## Slide 16: Capacitance
Breakdown voltage of materials
kV/mm
Air 3
Ceramic (high r) 3
Mica 40
Mylar 16
Oil 16
Polystyrene 24
Rubber 18
Teflon 60

## Slide 17: Capacitance
(iv) Temperature Coefficient
The physical size of the metal plates expand or contract with temperature.
The dielectric constant also varies with temperature.
Since the capacitance is directly proportional to these factors, the capacitance varies with temperature.
For capacitors with positive temperature coefficient the capacitance increases with increase in temperature.

## Slide 18: Capacitance
Negative temperature coefficient implies decrease in capacitance with increase in temperature.
Certain types of capacitors have near to zero temperature coefficient.
They are suitable for use in circuits which requires precise capacitance value.

## Slide 19: Capacitance
4. Type of Capacitors
Capacitors may be classified into
Fixed capacitors: the capacitance is fixed
Variable capacitors: the capacitance can be varied over a range

## Slide 20: Capacitance
Fixed Capacitors
Types of common fixed capacitors are
(i) Ceramic
(ii) Mica
(iii) Film
(iv) Electrolytic
(v) Surface mount

## Slide 21: Capacitance
(i) Ceramic Capacitors
relative dielectric constant of ceramic ranges from 10 to 10,000
temperature coefficient depends on the property of the ceramic used as the dielectric
Higher dielectric constant results in smaller capacitor size but higher temperature coefficient
temperature coefficient can be improved by using a mixture of material with positive temperature coefficient e.g. magnesium titanate and material with negative temperature coefficient e.g. calcium titanate
Typical value of ceramic capacitors ranges from a few pF to 0.5 F

## Slide 22: Capacitance
(ii) Mica Capacitors
relative dielectric constant of mica is around 5
low dielectric constant value makes mica capacitor size relatively larger than capacitors using other types of dielectric
very good temperature characteristic and suitable for use in circuits which requires stable capacitance.
cost of mica capacitor is higher than ceramic capacitors

## Slide 23: Capacitance
(iii) Film Capacitors
film capacitors are formed by placing a plastic dielectric such as polystrene, polycarbonate etc in between two sheets of metal foil
the sandwich structure is rolled into a cylinder shape to optimize the size of the capacitor
for metallized-film capacitors the metallic surfaces are formed by vacuum deposit method
the metal is vapourized and then deposit onto the plastic film surface in a vacuum container

## Slide 24: Capacitance
tight capacitance tolerance
the size is larger than ceramic capacitors of the same value
Electrolytic Capacitors
Aluminum electrolytic capacitors
use a thin layer of oxide as the dielectric
high dielectric constant
low breakdown voltage
polarized

## Slide 25: Capacitance
the most commonly used electrolytic capacitors is the capacitance can go up to 10,000 F or above
capacitance tolerance can be as large as +20%
temperature characteristics is poor
leakage current is high
suitable for use in circuits requiring large but not precise capacitance such as dc supply filtering

## Slide 26: Capacitance
Tantalum electrolytic capacitors
lower leakage current and more stable
smaller size
the capacitance only goes up to a few tens of F
The polarity of the connecting leads of electrolytic capacitors are marked on the capacitor.
Incorrect connection of these two leads in a dc circuit may cause damage to the capacitor.

## Slide 27: Capacitance
(v) Surface Mount Capacitor
miniature and leadless capacitors known as chip capacitors
suitable for printed circuit board with high component density
chip capacitors are surface mount components and an example of the size is 3mm x 3 mm x 1 mm.
the dielectric is usually ceramic
suitable for use in circuit boards with high component density and radio frequency circuits.
Metal plates
For soldering
Fig. 7

## Slide 28: Capacitance
Variable Capacitors
The capacitance of a variable capacitor can be varied over a small range.
The capacitor consists of a set of fixed plates and a set of movable plates with air as the dielectric.
Movable
plate
Fixed
plates
Fig. 8

## Slide 29: Capacitance
The fixed plates are connected by metal conductors.
The overlapping area of the movable and fixed plates depends on the angular position of the movable plate.
The overlapping is related to the area A and distance d of the equation of capacitance C = Q/A.
Hence the capacitance can be changed by rotating the movable plate to different position.
By increasing the number of the interleaving plates the capacitance can reach several hundred pF.

## Slide 30: Capacitance
5. Capacitors connected in parallel
When two capacitors are connected in parallel as shown Fig. 9, the voltage across the two capacitors are equal.
The charge in C1 is Q1 and in C2 is Q2.
The total charge stored in the 2 capacitors is
V
Fig. 9
C1
C2

## Slide 31: Capacitance
The total capacitance of 2 capacitors connected in parallel is equal to the sum of the capacitance of the 2 capacitors.
Example: A capacitor of 0.2 F is connected in parallel with a capacitor of 150 nF.
Solution: The total capacitance

## Slide 32: Capacitance
The same derivation can be extended to any number of capacitors connected in parallel.
The total capacitance is simply the sum of all the capacitors connected in parallel.

## Slide 33: Capacitance
6. Capacitors connected in series
The charge stored in each capacitor is the same and equal to Q.
and
V
Fig. 10
C1
C2
V1
V2

## Slide 34: Capacitance
The same derivation can be extended to any number of capacitors connected in series giving

## Slide 35: Capacitance
Example: Find (i) the total capacitance of the circuit
shown in Fig. 11
(ii) the voltage across each capacitor
Fig. 11
C1
2.2 F
C2
10F
C3
0.1F
12V

## Slide 36: Capacitance
Solution:
(i) The total capacitance
(ii) Since
The voltage across
The voltage across
The voltage across

## Slide 37: Capacitance
The calculation shows that
the total capacitance of capacitors in series is less than the capacitance of the smallest capacitor
the voltage across the smallest capacitor is highest of all the capacitors in series