## Slide 1
Resistance
PART 2
Reference Book: Circuit Analysis by Robbins & Miller

## Slide 2
5 Types of Resistors (p. 72)
Fixed Resistors
Having resistance values which are essentially constant.
Ranging in size from almost microscope (in IC) to high-power resistors
Carbon composition resistor [Fig. 3-7, p. 72]
The ratio of carbon to insulating filler determines the resistance value of the resistor.
Resistance ranges from less than 1 ohm to 100 Mohm.
Power ratings from 1/8 W to 2W.
Adv.: inexpensive and easy to produce.
Disadv.: wide tolerances and high temp coefficient [Fig. 3-9, p. 73].

## Slide 3
Fig. 3-7 Structure of a molded carbon composition resistor (p. 72)

## Slide 4
Fig. 3-9 Variation in resistance of a carbon resistor (p. 73)

## Slide 5
Metal film
Desired resistance is obtained by removing part of the resistive material, resulting in a helical pattern around the ceramic core.
Adv.: small temp coefficient and high precision.
Disadv.: higher cost.
Wire-wound
Constructed of a metal alloy wound around a hollow porcelain core.
Adv.: able to dissipate large quantities of heat.
Disadv.: higher inductance.

## Slide 6
Integrated resistor
Constructed in miniature IC packages.
Adv.: conserve space in circuit board
Disadv.: used in circuit where dissipation of heat is not a major design consideration.
Variable Resistors
Used to adjust the volume of radios, and set level of lighting.
Three terminals. Two of which are fixed to the ends of resistive materials [Fig. 3-13]. Central terminal is connected to a wiper which moves over the resistive material.

## Slide 7
Fig. 3-12 Variable Resistors (p. 75)

## Slide 8
Fig. 3-13 Variable Resistors and Terminals (p. 76)

## Slide 9
Rac = constant
= Rab + Rbc
Functions: Potentiometer [Fig. 3-13c] – adjust voltage.
Rheostat [Fig. 3-14] – adjust current.
Fig. 3-14 Rheostat (p. 76)

## Slide 10
6. Color Coding of Resistors (p. 76)
Small resistors are too small to have their values printed on the component. Instead, color bands are used. [Fig. 3 – 15, p. 77]
The color bands are always read from left to right, left being defined as the side of the resistor with the band nearest to it.
Band 1 and 2 : first are second digits of the resistance value.
Band 3 : Multiplier band - represent s the number of zeros
following the first two digits given as a power of ten.
Band 4 : tolerance value
Band 5 : (if present) indicates the expected reliability.
[Reliability - statistical indication of the expected number of components which will no longer have the indicated resistance value after 1000 hours of use.]

## Slide 11
Fig. 3 – 15 Color codes (p. 77)

## Slide 12
Table 3-5 Resistor Color Codes (p. 78)

## Slide 13
Solution From Table 3 - 5, we see that the resistor will have a valuedetermined as
R = 18 x 103  + 5%
= 18k + 0.9k with a reliability of 0.1%
This specification indicates that the resistance will fall between 171k and 189k. After 1000 hours, we would expect that no more than 1 resistor in 1000 would fall outside the specified range.

## Slide 14
Question : Find the value and tolerance of a resistor if the color bands reading from left to right are
Red, yellow, orange, gold
Assignment : (Ch. 3) Problem 25, 27, 29, 31, 33

## Slide 15
7 Measuring Resistance - The Ohmmeter (p. 78)
Multimeter - measure voltage (voltmeter), current (ammeter), and resistance (ohmmeter)
Use of ohmmeter :
measure resistance of components
determine whether a circuit is faulty (i.e. open and short circuit)
determine the condition of semiconductor devices such as diodes and transistors.

## Slide 16
Measure resistance in a circuit [Fig. 3 – 19, p. 80]

## Slide 17
Measure resistance of component which is located in an operating circuit.
disconnect power supplies [Fig. 3 - 19a]
isolate the component from the rest of circuit [Fig. 3 - 19b]
connect two probes of ohmmeter across the component
ensure ohmmeter is on correct range
turn ohmmeter off
Measure the continuity of a circuit.
Short circuit
- ohmmeter will indicate a very low ( 0 ) resistance.
Open circuit
- ohmmeter will indicate infinite resistance.
[Practical Notes] - reading of ohmmeter in open circuit
[Practice Problem VI]

## Slide 18
Figure 3 - 20

## Slide 19
8. Thermistors (p. 81)
Transducer - device or component which causes an electrical
change due to a physical change.
Thermistor (thermal resistor) - 2-terminal transducer in which
resistance changes with changes in temp.
Symbol : [Fig. 3 - 21 and 3 - 22]

## Slide 20
Construction :
oxides of various materials such as cobalt, manganese, nickel, and strontium
Negative temp coefficient :
as temp increases, the outmost electronics in the atoms of material become more active and break away from atom which causes a reduction in resistance. [Fig. 3-22, p. 82] [Practice Problem VII]
Use in circuits to :
control current
measure of control temp
Applications :
electronic thermometer
thermostatic control circuits for furnaces

## Slide 21
Fig. 3 – 22 Thermal resistance as a function of temp (p. 82)

## Slide 22
9. Photoconductive Cells (Photocells) - (p. 82)
Two terminal transducers which have resistance determined by the amount of light falling on the cell. [Fig. 3 - 23(a)]
Symbol : [Fig. 3 - 23(b)]

## Slide 23
Construction :
cadium sulfide (CdS), cadium selenide (CdSe)
sensitive to light having wavelengths between 4000Å (blue light) to 10000Å(infrared) [Noted : 1Å = 1 x 10-10 m)]
Negative temp coefficient: [Fig. 3 - 23 (c)]
light, which is a form of energy, strikes the material of photocell and causes the release of electronics, and hence reduce the resistance.
Use in circuits to : measure light intensity and/or control lighting.
Applications : used as part of a security system.
Assignment : (Ch. 3) Problem 35, 37, 39, 40

## Slide 24
Fig. 3 - 23 (c) Resistance vs illumination

## Slide 25
10. Resistance in Series
Equivalent resistance of a series of resistors is the summation of all resistances.
R(equivalent) = R1 + R2 + R3 + …

## Slide 26: 11. Resistance in Parallel Equivalent resistance of a set of resistors connected in parallel is 1/R(equivalent) = 1/R1 + 1/R2 + 1/R3 + ...