## Slide 1: Real-Time Detection and Tracking of Human Eyes in Video Sequences
Zafer SAVAŞ
METU-EE 2005

## Slide 2: Outline
Aim and rationale of the study
Previous work related to our study
  Studies related to eye
  Studies related to face
Detailed explanation of our approach
  Face Detection
  Adaptive EigenEye method
  Feature Extraction
Results, comments and conclusions
0 min
5 min
10 min
20 min
25 min

## Slide 3: Aim
In general, eye detection is used when static face images are of the concern and main aim is the extraction of all facial features.
Eye tracking is used as a part of continuously detection of facial features in video sequences where the frames contain only face images.
Our aim is to give detailed information such as
  The contour of the visible eyeball region
  Circular area formed by iris and pupil
  Location of pupil in the visible eye area
  State of the eye (blink/not blink)

## Slide 4: Aim
Properties of the system we aimed to design were:
  Video frames are not only face images
  Features of the eyes are tracked: Pupil area and visible eye ball area
  Coordinate informations and direction of sight is extracted
  Eyes are tracked individually
  Scale and rotation invariance
  Cost effective; Compatible with a standard PC environment and simple setup
PC with a
necessary SW
Camera

## Slide 5: Summary of our Approach
There are 3 milestones of our approach
  Scale invariant face detection
  Individual eye area detection in the face area
  Extraction of visible eye features
After features are detected, necessary coordinate informations and direction of gaze information are found.

## Slide 6: Summary of our Approach
Left
Right
Calculations for indications are performed

## Slide 7: Summary of our Approach
Decisions taken before the start of the study were :
  During our study we wanted all of our methods to rely on reliable and fast previous methods.
  No assumption based methods shall be considered.
  Although there has been a lot of previous techniques developed for face and eye detection, we shall try to develop techniques which were not previously implemented.
  All the theoretical study shall be realized by a software implementation.

## Slide 8: Previous work related to our study - Eye
There has been a lot of previous work related to eyes;
  Eye area detection
  Eye feature extraction
  Measurement of eye movements
  Eye state detection
We can classify studies related to eye into two main categories:
  Special equipment based approaches
  Image based approaches

## Slide 9: Special Equipment based approaches
Using necessary equipment which will give a signal of some sort which is proportional to the position of the eye in the orbit, and changes when the position of the eye changes in some direct way is an accurate way of measuring eye position but it is impractical and expensive compared to the image based methods.
Various methods that are currently in use are:
- Electrooculography
- Infra-Red Oculography
- Scleral search coils

## Slide 10: Image based approaches
Eye detections are performed on the images.
IR based methods rely on the spectral properties of the eye pupil under IR illumination. The camera is able to detect the the light reflected from the interior of the eye. This is also out of our scope.
Eyes and features are detected using the features of the eyes. Methods used so far are knowledge-based methods, feature-based methods (color, gradient), simple template matching, appearence methods. We have developed an appearence-based method called adaptive eigeneye method.
Deformable template matching : Developed by Yuille and Hallinen. Geometrical and Imaging models are deformed with the matching algorithm over the image.

## Slide 11: Previous work related to our study - Face
First problem for our automatic eye tracking system is the detection of human face in image sequences. There about 150 different techniques for face detection in images. Our requirements were;
- Must be fast
- Must be independent of the complex background
- Must be independent of the structural components of face
According to the surveys, methods can be classified as 4 categories;
- Knowlegde-based methods
- Feature invarient Approaches
- Template matching
- Appearance-based methods

## Slide 12: Previous work related to our study - Face
Knowledge-based methods : These methods use simple rules to describe features of a face such as; a face often appears in an image with two eyes that are symmetric to each other, a nose and a mouth. The relationships between features can be represented by their relative distances and positions.
Feature invariant methods : These algorithms aim to find structural features that exist even when the pose, viewpoint, or lightening conditions vary.
Template matching : Given an input image, the correlation values with the standard patterns are computed for face contour, eyes, nose, mouth.
Appearance-based methods : In contrast to template matching, templates are learned from a set of training images.Appearance-based methods rely on techniques from statistical analysis and machine learning.

## Slide 13: Implementation
The implementation is based on three independent components:
1) Face detection component
2) Eye detection component
3) Eye feature extraction component
Face Detector
Eye Detector
Feature Extractor

## Slide 14: Implementation – Face Detector
The face detection algorithm implemented in this study is a feature-based face detection method and uses the Continuosly Adaptive Mean-Shift algorithm.
CAMSHIFT algorithm is based on robust, non-parametric technique called mean-shift algorithm for climbing gradients to find the center of the probability distributions.
Probability distribution is the probability of an area to be skin.
So; infact we are detecting the skin color, not the face.

## Slide 15: CAMSHIFT Algorithm – HSV
To form the probability distribution images CAMSHIFT uses the HUE component of the HSV images.
HUE component of HSV is the most proper for skin detection
At low brightness and saturation HUE is quite noisy. So those pixels are ignored.
It works well with a wide varity of people

## Slide 16: CAMSHIFT Algorithm
Zeroth moment :
First order moment :
Centroid :
Here I(x,y) is the pixel probability value at position (x,y) in the probability image. x any y range over the search window.
Calculation region : is the image area where the probability distribution is calculated.
Search window : is the area considered during mean-shift.

## Slide 17: CAMSHIFT Algorithm
Start
Prompt user for
a sample hue region
Grab a new image frame
Construct probability image
in the calculation region
Resize the search window
To catch the outline of the face
As a result of the algorithm, search window converges to span the nearest dominant connected probability disribution.

## Slide 18: CAMSHIFT-Visualization
Calculation Window
Sample HUE
Search Window

## Slide 19: CAMSHIFT Algorithm
Easy to implement
Works with cheap cameras as the algorithm is robust to noise
Doesn’t require too much computational resources
Defining sample hue is an important initialization step
Independent to items on face such as beard, glasses.
High or low illumination makes the algorithm fail.
Robust to variable ambient lighting
Overlapping regions with the face area
Distractors around the face are easily ignored
Disadvantages
Advantages

## Slide 20: Implementation - Eye Detector
Eye detection component is based on Eigenface method proposed by Turk&Pentland which is a Principal Component Analysis approach.
The main idea is to decompose face images into a small set of characteristics feature images called eigenface, which may be thought of as the principal components of the original images. These eigenfaces function as the orthogonal basis vectors of a subspace called face space.
Eigenfaces characterizes the variation between face images.
Instead of face we are detecting eyes. So we called our method as eigeneye detection.

## Slide 21: Eigenface method
Construction of the face space
1) Γ is an NxN face image. It can be represented as a 1D vector of size N2
2) Average image of the database is
3) Covariance Matrix is formed by C = A.AT where A = [Φ1 ... Φm ]
The size of C is N2xN2. The eigenvectors of the covariance matrix forms the feature vector (transformation matrix)
Detection of face
1) A new image is projected onto the face space by
2) Reconstruct the original image by
3) The euclidian distance between the original image and the reconstructed image is calculated to understand if the image is a face or nonface

## Slide 22: EigenFace Method
Small sized images may not have distinguisable features
Not suitable for real-time applications
Detection process is a simple step of the whole algorithm
The algorithm is not scale invariant
Implementation
Disadvantages
Advantages
!! So we have developed the adaptive eigeneye detection !!

## Slide 23
Adaptive Eigeneye method
EyeWidth / FaceWidth ≈ 0.35

## Slide 24: Implementation - Feature extraction
Considering an eye image, the eye area can be partitioned into 2 simple overlapping regions which may be accepted as the features of human eye;
Region#1 : The area occupied by iris and pupil parts of the eye
Region#2 : The visible eyeball area. Region#2 contains region#1

## Slide 25: Implementation - Feature extraction
Region#1 Detection
Region#2 Detection
Start
and
Change colorspace
select component
Binary threshold
Edge detection
Circle detection
Start
and
Change colorspace
select component
Adaptive threshold
Edge detection
Minimize Active Contour energy

## Slide 26: Region#1 Detection

## Slide 27: Active Contours
There are three types of energy defined for a snake
  Elastic energy : This energy tries to increase the total length of the snake
  Bending energy : This energy makes the snake behave like a metal strip rather than an elastic band. By this energy, snake is a smooth curve.
  Image gradient energy : This energy produces a force to drive the snake points to the image edges.

## Slide 28: Region#2 Detection
Hue component of the HSV color space shall be used to get rid of the skin color
Adaptive thresholding is used instead of global thresholding because there may be illumination gradients in the eye area

## Slide 29: TrackEye software
Adjustments that the user has to make before the tracking:
1) Camera adjustment
2) Hue definiton
3) Eye database
4) Threshold levels for Region#1-2

## Slide 30: Results&Comments

## Slide 31: Results & Comments
+ | -
Parameters defined by the user are simple | System performance is dependent on the parameters defined by the user
Requires simple eye database for adaptive eigeneye detection | Performance of the whole system is dependent on the face detection module
Requires simple setup PC+webcam+Software | Face detection is performed by skin detection
Works with cheap cameras | Camera adjsutment shall be done by the user
Scale and rotation invariant | 

## Slide 32: Application Areas
Aviation
Driver monitoring systems
Helping disabled people
Research related applications
Security systems
Clinical diagnostics
Marketing and advertising
Computer games